CANPiWi User guide

# How it works

The CANPiWi is a module designed considering 2 major features:
- to allow the user control some aspects of the layout using the EngineDrive (ED) application without JMRI and using wireless connections.
- to allow other devices to interact with CBUS using the GridConnect protocol using wireless connections.

The module allows smartphones using EngineDrive or/and other devices using the GridConnect to connect to the module using the TCP/IP protocol. Once the devices are connected the module does the protocol translation from ED to CBUS and the other way around and also from GridConnect to CBUS in both directions.

The CANPiWi allows the connection via wifi in two modes:
- as access point mode (AP mode)
- or as client mode (WIFI mode)

In AP mode, the module is responsible to create a local TCP/IP network. Any device connected will be assigned a unique IP for that network via DHCP (Dynamic Host Configuration Protocol) service. The module will announce the ED service on the IP 192.168.1.45.
In WIFI mode, the module has to connected to an existing router that will assign the module an ip address. The module will announce the ED service on that given ip.

The service announcement uses the Bonjour protocol. Bonjour is Apple's implementation of zero-configuration networking (zeroconf), a group of technologies that includes service discovery, address assignment, and hostname resolution.

# Turning the module on
Once the module is powered, a red light will indicate that the module is energised and either the green led or the yellow led will be on. The green led on means that the module is in SLIM mode and is using the default configuration for node number and can id. The default values are:
node number = 300
can id = 100

If none of the lights are on please check the troubleshooting section of this document.

If the module is proper powered and connected to a CBUS will generate an ON CBUS short event to indicate it is powered and operational. If the ED or GridConnect service is restarted it will generate an Off followed by an ON event.

# Connecting
The connection changes depending on the mode the module is working. The module, by default comes with AP mode configured. To change that see the Configuration section.
## AP mode
In AP mode the module will create a wifi ssid with name “CANPiWi” by default. The ssid name can be changed by changing the configuration (see the configuration section). You should be able to see the ssid using any device that detects access point, like smartphone, tablets or PC/Laptops.
Use the device procedure to connect to a wifi network to connect to the “CANPiWi”. If the connection fails, try again, and if it still fails check the troubleshooting section.

Once connected you can open the ED in the smartphone. On the main screen of the ED there might be an entry for “MyLayout” on port 5555. See the image below.

[TODO: Add image]

Click on item “MyLayout” and the ED will request a connection to the CANPiWi. Once the connection is done you can select an existing loco or enter a new one.
## WifiMode
In WIFI mode the module needs to be connected to an existing wifi network. To allow that you need to change the configuration for WIFI mode and provide the ssid and the access password for the wifi network. The ssid and password have to be correctly informed, otherwise the module won’t be able to connect. If the connection does not work, then the module has to be reseted to AP mode and you can try again. See the section “Reset to AP mode” for more information.

If the connection is successfull you might the able to see the ED service advertised in the ED screen. If not please proceed to the troubleshooting section.
Once connected you can click on service advertised by in the ED screen and it proceed to connect to the CANPiWi.
Normally the home routers should not block the port 5555 for internal connection. If the connection does not work check if the firewall in the router is activated and if the port 5555 is open. If that is not the problem, check the troubleshooting section.

# Configuration

The CANPiWi module provide several parameters for configuration. We divide there configuration parameters in:
- wifi parameters
- CBUS parameters
- general parameters

There are also 3 ways of configuring the module:
- using an embebeded webpage
- using the FCU
- manual editing

The configuration is stored in a file called canpi.cfg in the /home/pi/canpi directory in the SD card.
## Parameters

List of all parameters keys present in the canpi.cfg

Parameter	Configuration type
canid	CBUS
node_number	CBUS
start_event_id	CBUS
button_pin	General
can_grid	General
candevice	General
cangrid_port	General
create_log_file	General
fn_momentary	General
green_led_pin	General
logappend	General
logfile	General
loglevel	General
service_name	General
tcpport	General
turnout_file	General
yellow_led_pin	General
ap_channel	Wifi
ap_mode	Wifi
ap_no_password	Wifi
ap_password	Wifi
ap_ssid	Wifi
router_password	Wifi
router_ssid	Wifi

### Wifi parameters
AP/Wifi mode
This parameter indicates if the module has to work as an AP or connect to another wifi network.
AP mode without password
If the module is in AP mode no password is required. It means the user just need to connect to the module ssid and no password will be required. If the property is set, then the “AP password” parameter has to be informed.
AP ssid name
The wifi network name that will be shown to another device. This parameter is the network name of the module. It is required if the module is in “AP mode”.
AP password
The password required to connect to the module when in “AP mode” and “AP mode without password” is not set.
AP wifi channel
The wifi channel that the module will work. The channels are from 1 to 13. For more infomation see https://en.wikipedia.org/wiki/List_of_WLAN_channels
The non overlapping channels are:
- 1, 6, 11 or
- 2, 7, 12 or
- 3, 8, 13
The choice of the channel will depend on the presence of other access points (APs) in the same area. APs with the same channel may affect each other and jam the communication between the clients and the module. The module value by default is 6 [TODO: check].
Router ssid
The ssid of the router that the module will connect to when in “WIFI mode”. It has to be exactly value advertised by the other router.
Router password
The password of the router that the module will connect to when in “WIFI mode”. It has to be exactly value expected by the other router.
### CBUS parameters

Start event id

This parameter indicates the short event number that will be generated when the ED and GridConnect service starts. An ON event will be triggered on start and an OFF event will be triggered id the service gracefully stops.

Node number

The module node number. This value is changed on by doing the request node number procedure common to all Merg CBUS modules. A manual change can clash with other modules and make the CBUS instable.

### General parameters
Service name

The service name announced to EDs. This is the name that will show in the first screen of ED when connected to the same network of the CANPiWi.

TCP Port

The tcp port that the ED service accepts connection. This value will be displayed in the ED screen.

GridConnect port

The tcp port that the GridConnect service accepts connection.

Enable grid connect

Enable or disable the GridConnect service to run.

Turnout file

A file name stored inside the CANPiWi with the turnout definition. See the section Configuring the turnout file [TODO].

Log file

The log file name stored inside the CANPiWi. This file is mostly used for debug purpouse. It is reseted every time the module starts. In case the module stay on for several time without reset the size is limited by 50Mbytes.

Log level

Indicates the granularity of the information present in the log file. The possible levels are:
- INFO
- WARN
-DEBUG

DEBUG level is the mostly verbose mode of them.

Log append

Indicates if the log file should be created.

Fn momentary

Specifies which Fn key has the momentary behaviour by default. The standard value is 2. The values can be a list of comma separated values. The user also can create values that are specific for locomotive numbers. See “Fn configuration” section for more information.

Web configuration

FCU configuration

Engine Drive

Locomotive control

Turnout control

Fn configuration

Grid connect

Upgrading process

Troubleshooting